Motors (x4)	GHM-03 Spur Gear Head Motor	Powered via H-Bridge
H-bridge (x4)	Cytron MD10C Motor Drivers	4x 12V Batteries each with 2 ports each
Arduino Uno (lower)	MotorA - PWM Pin 11, Dir Pin 13, front left / MotorB - PWM Pin 10, Dir Pin 12, Rear left / MotorC - PWM Pin 9, Dir Pin 7, Front right / MotorD - PWM Pin 6, Dir Pin 8, Rear right / I2C to upper Arduino - Pins A4 (purple wire is in A4 which connects to black in extender in middle), A5 (white wire is in A5 which connects to red in extender in middle)	Connected to 12V battery
Arduino Uno (upper)	I2C to lower Arduino - Pins A4, A5 / Serial to Servo board - Pin 0 (orange Rx), Pin 1 (red Tx) / Infrared sensor - digital pin 10 / Sonar pulse sensor - Trig pin 13, Echo pin 7 / Motion sensor - digital pin 12 / USB to Raspberry Pi 1	Arduino connected to 12v battery / Sensors connected to ?
Servo control board Lynxmotion SSC32U	Servo 0 - Turret with LCD / Servo 1 - 6 - Robotic arm (6 degrees of freedom) / Servo 7 - sonar sensor rotation / Servo 8 - 10 - unused but wired	Connected to 5V/2.1amp portable iphone battery pack
Raspberry Pi 1 (Voice AIY)	USB to Arduino Uno (upper) / GPIO to Voice Hat / USB to Raspberry Pi 2 / USB to Raspberry Pi 3
Raspberry Pi 2 (Vision AIY)	GPIO to Vision Hat / USB to Raspberry Pi 1
Raspberry Pi 3 (LCD)	GPIO to LCD / USB to Raspberry Pi 1
Google API console
Github